## Slide 1: 15IT303J
COMPUTER
NETWORKS
15IT303J | COMPUTER NETWORKS

## Slide 2: UNIT I : INTRODUCTION TO COMPUTER NETWORKS
Evolution of Computer Networks
Classification of Computer Networks LAN,WAN,MAN
Network Topology : BUS, STAR, RING, MESH -
OSI Layered Architecture
TCP/IP Model

## Slide 3: Outline
Data Communication Overview
  Definition
  Components
  Protocols and standards
Network Overview
  Connectivity
  Categories
  Internetworks

## Slide 4: Motivations
Efficient way to share resources
  Cost – less expensive
  Accessibility – easier
Efficient way to exchange information
  Time – faster
  Size – bigger
  Correctness – more accurate

## Slide 5: Data Communication: Definition
Data Communication:
Transfer of data from one device to another via
some form of transmission medium.

## Slide 6: Data Communication
Hi, how are you?
01010001
Hi, how are you?
Computer
you?
how
are
Hi,
you?
how
are
Hi,
01010001

## Slide 7: Components in Communication
Hi, how are you?
5
Protocol
4
Medium
3
Receiver
2
Sender
1
Message

## Slide 8: Data Representation
Numbers
  8/16/32 bit integers
  floating point
Text
  ASCII, Unicode
Images
  Bit patterns, Graphics formats JPG/GIF/etc
Audio  Samples of continuous signal
Video  Sequence of bitmap images
150
2
255

## Slide 9: Protocols and Standards
Protocol
  A set of rules governing data communications
    Syntax: format of data block
    Semantics: meaning of each section
    Timing: speed and sequencing
Standards
  De facto (in practice) standards
     not approved but widely adopted
  De jure (in law) standards
     approved by an organization

## Slide 10: Standards Organizations
Creation Committees
  ISO, ITU-T, ANSI, IEEE, EIA
Forums
Regulatory Agencies

## Slide 11: Direction of Data Flow
Simplex: One direction only
Server
Monitor
data flow
Keyboard
data flow

## Slide 12: Direction of Data Flow
Half Duplex: Both directions, one at a time
  E.g., walkie-talkies
data flow at time 1
data flow at time 2

## Slide 13: Direction of Data Flow
Full Duplex: Both directions simultaneously
  E.g., telephone
Can be emulated on a single communication link using various methods
data flow
data flow

## Slide 14: Networks
Network: a set of devices connected by media links
Media Links
Printer
Workstation
Laptop
Scanner
Server

## Slide 15: Types of Connections
Point-to-point
Multipoint (multidrop)

## Slide 16: Point-To-Point Connection

## Slide 17: Multipoint Connection
Wireless

## Slide 18: Topology
Topology: physical or logical arrangement of devices
  Point-to-point
  Mesh
  Star
  Bus
  Ring
  Hybrid

## Slide 19: Point-to-Point Connection

## Slide 20: Fully Connected Mesh Topology
A
C
B
D
E

## Slide 21: Fully Connected Mesh Topology

## Slide 22: Fully Connected Mesh Topology
Pros:
  Dedicated links
  Robustness
  Privacy
  Easy to identify fault
Cons:
  A lot of cabling
  I/O ports
  Difficult to move

## Slide 23: Star Topology
Hub
A
D
B
C
Drop
Drop

## Slide 24: Star Topology
Switch
A
D
B
C

## Slide 25: Star Topology
Hub
A
D
B
C

## Slide 26: Star Topology
Pros:
  One I/O port per device
  Little cabling
  Easy to install
  Robustness
  Easy to identify fault
Cons:
  Single point of failure
  More cabling still required
Hub

## Slide 27: Bus Topology
Drop line
Tap
Terminator

## Slide 28: Bus Topology
A
B
C
D

## Slide 29: Bus Topology

## Slide 30: Bus Topology
Pros:
  Little cabling
  Easy to install
Cons:
  Difficult to modify
  Difficult to isolate fault
  Break in the bus cable stops all transmission

## Slide 31: Ring Topology
A
B
C
D

## Slide 32: Ring Topology

## Slide 33: Ring Topology
Pros:
  Easy to install
  Easy to identify fault
Cons:
  Delay in large ring
  Break in the ring stops all transmission

## Slide 34: Hybrid Topologies

## Slide 35: Network Categories
Local Area Network (LAN)
Wide Area Network (WAN)
Metropolitan Area Network (MAN)

## Slide 36: Local Area Networks
Network in a single office, building, or campus

## Slide 37: Wide Area Networks
Network providing long-distance communication over a country, a continent, or the whole world

## Slide 38: WAN Technologies
Circuit Switching
  Physical links are dedicated between two points
Packet Switching
  Data are put in packets which are stored and forwarded at each node
Virtual Circuit Switching
  Virtual links are established between two points
   Frame Relay and ATM (Asynchronous Transfer Mode)

## Slide 39: Metropolitan Area Networks
Network extended over an entire city
Bangkhen
Kampangsaen

## Slide 40: Switching
Dedicated circuits
Circuit switching
  Telephone switches establish circuits for communication
Packet switching
  Data are put into packets
  Each stamped with source and destination addresses
  Routers know where to forward packets
telephone switch
Router
Packet

## Slide 41: Network of Networks
Company A
Company D
Network Interface Card (NIC)
Company B
Company C

## Slide 42: Internetworking
How to allow devices from different standards to communicate
Gateways/routers – devices capable of communicating in several standards
These become "network of networks"

## Slide 43: Internetworks
Two or more networks connected become an internetwork, or internet
Example: The Internet
Network1
Network2
Gateway
Network3

## Slide 44: The Internet
The largest internetwork (network of networks) in the world
Devices communicating with TCP/IP protocol suite
UCLA
Stanford
UC Santa Barbara
U. of Utah

## Slide 45: Summary
Data communication
  Protocols and standards
Computer networks
  Topologies
  LAN/MAN/WAN
Internetworks (networks of networks)

## Slide 46
2-1 LAYERED TASKS
We use the concept of layers in our daily life. As an example, let us consider two friends who communicate through postal mail. The process of sending a letter to a friend would be complex if there were no services available from the post office.
Sender, Receiver, and Carrier Hierarchy
Topics discussed in this section:

## Slide 47
Figure 2.1 Tasks involved in sending a letter

## Slide 48
2-2 THE OSI MODEL
Established in 1947, the International Standards Organization (ISO) is a multinational body dedicated to worldwide agreement on international standards. An ISO standard that covers all aspects of network communications is the Open Systems Interconnection (OSI) model. It was first introduced in the late 1970s.
Layered Architecture Peer-to-Peer Processes
Encapsulation
Topics discussed in this section:

## Slide 49
ISO is the organization. OSI is the model.
Note

## Slide 50
Figure 2.2 Seven layers of the OSI model

## Slide 51
Figure 2.3 The interaction between layers in the OSI model

## Slide 52
Figure 2.4 An exchange using the OSI model

## Slide 53
2-3 LAYERS IN THE OSI MODEL
In this section we briefly describe the functions of each layer in the OSI model.
Physical Layer Data Link Layer
Network Layer
Transport Layer
Session Layer
Presentation Layer
Application Layer
Topics discussed in this section:

## Slide 54
Figure 2.5 Physical layer

## Slide 55
The physical layer is responsible for movements of
individual bits from one hop (node) to the next.
Note

## Slide 56
Figure 2.6 Data link layer

## Slide 57
The data link layer is responsible for moving frames from one hop (node) to the next.
Note

## Slide 58
Figure 2.7 Hop-to-hop delivery

## Slide 59
Figure 2.8 Network layer

## Slide 60
The network layer is responsible for the delivery of individual packets from
the source host to the destination host.
Note

## Slide 61
Figure 2.9 Source-to-destination delivery

## Slide 62
Figure 2.10 Transport layer

## Slide 63
The transport layer is responsible for the delivery of a message from one process to another.
Note

## Slide 64
Figure 2.11 Reliable process-to-process delivery of a message

## Slide 65
Figure 2.12 Session layer

## Slide 66
The session layer is responsible for dialog control and synchronization.
Note

## Slide 67
Figure 2.13 Presentation layer

## Slide 68
The presentation layer is responsible for translation, compression, and encryption.
Note

## Slide 69
Figure 2.14 Application layer

## Slide 70
The application layer is responsible for providing services to the user.
Note

## Slide 71
Figure 2.15 Summary of layers

## Slide 72
2-4 TCP/IP PROTOCOL SUITE
The layers in the TCP/IP protocol suite do not exactly match those in the OSI model. The original TCP/IP protocol suite was defined as having four layers: host-to-network, internet, transport, and application. However, when TCP/IP is compared to OSI, we can say that the TCP/IP protocol suite is made of five layers: physical, data link, network, transport, and application.
Physical and Data Link Layers Network Layer Transport Layer
Application Layer
Topics discussed in this section:

## Slide 73
Figure 2.16 TCP/IP and OSI model

## Slide 74
2-5 ADDRESSING
Four levels of addresses are used in an internet employing the TCP/IP protocols: physical, logical, port, and specific.
Physical Addresses Logical Addresses Port Addresses Specific Addresses
Topics discussed in this section:

## Slide 75
Figure 2.17 Addresses in TCP/IP

## Slide 76
Figure 2.18 Relationship of layers and addresses in TCP/IP

## Slide 77
In Figure 2.19 a node with physical address 10 sends a frame to a node with physical address 87. The two nodes are connected by a link (bus topology LAN). As the figure shows, the computer with physical address 10 is the sender, and the computer with physical address 87 is the receiver.
Example 2.1

## Slide 78
Figure 2.19 Physical addresses

## Slide 79
Most local-area networks use a 48-bit (6-byte) physical address written as 12 hexadecimal digits; every byte (2 hexadecimal digits) is separated by a colon, as shown below:
Example 2.2
07:01:02:01:2C:4B
A 6-byte (12 hexadecimal digits) physical address.

## Slide 80
Figure 2.20 shows a part of an internet with two routers connecting three LANs. Each device (computer or router) has a pair of addresses (logical and physical) for each connection. In this case, each computer is connected to only one link and therefore has only one pair of addresses. Each router, however, is connected to three networks (only two are shown in the figure). So each router has three pairs of addresses, one for each connection.
Example 2.3

## Slide 81
Figure 2.20 IP addresses

## Slide 82
Figure 2.21 shows two computers communicating via the Internet. The sending computer is running three processes at this time with port addresses a, b, and c. The receiving computer is running two processes at this time with port addresses j and k. Process a in the sending computer needs to communicate with process j in the receiving computer. Note that although physical addresses change from hop to hop, logical and port addresses remain the same from the source to destination.
Example 2.4

## Slide 83
Figure 2.21 Port addresses

## Slide 84
The physical addresses will change from hop to hop,
but the logical addresses usually remain the same.
Note

## Slide 85
Example 2.5
A port address is a 16-bit address represented by one decimal number as shown.
753
A 16-bit port address represented as one single number.

## Slide 86: Outline
Circuit vs. packet switching
Layered tasks
Internet protocol suites
ISO's OSI model

## Slide 87: End-to-End Communication
Direct communication
  Most basic form of communication
Internet communication
  Communication is performed over the Internet
TX
TX
RX
RX
GND
GND
Serial Port
Internet

## Slide 88: Internet Comm. - App's Viewpoint
Two network applications should interact as if they were directly connected
But what's going on underneath?
  What is inside the "cloud"?
Internet
A
App
B
App
write
read

## Slide 89: Circuit vs. Packet Switching
Early communication networks
  Dedicated circuit
Electronic switches are used
  Circuit switching
In 1960s, packet switching concept revolutionized data communications
  Provides the basis for the modern Internet
  Allows multiple users to share a network
  Divides data into small blocks, called packets
  Includes an identification of the intended recipient in each packet

## Slide 90: Circuit vs. Packet Switching
Dedicated circuits
Circuit switching
  Telephone switches establish circuits for communication
Packet switching
  Data are put into packets
  Each stamped with source and destination addresses
  Routers know where to forward packets
telephone switch
Router
Packet

## Slide 91: Layered Tasks
Computer networks are complex systems
  Tasks involve varieties of hardware and software components, and protocols
Networking task is divided into several subtasks, or layers

## Slide 92: Real World Example
Communication between managers of two companies
Communicate

## Slide 93: What Actually Happens
Communication takes place thru many layers
Logical communication
Secretary: types a letter
Delivery boy: drops the letter
Secretary: reads and reports the message
Delivery boy: takes the letter
Post office:
Processes and routes the letter
Postal truck

## Slide 94: Layer Model
Layer N uses services provided by Layer N-1
Layer N
Layer N
Using services
Providing services
Logical communication path
HOST A
HOST B
Layer N-2
Layer N-2
Layer N-1
Layer N-1
Virtual Communication System
Layer N protocol

## Slide 95: Why Layers?
Guidelines for protocol developments
  Reference model
Modularity
  Eases maintenance and updating of systems
  A change in one layer is transparent to the rest
Is layering always the best thing to do?
  Maybe not  cross-layer optimization

## Slide 96: Internet Layer Model
The Internet Protocol Stack
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
User
Transmission Medium
Hardware
Software

## Slide 97: Application Layer
The only layer to interact with user
Responsible for providing services to the user
SMTP
HTTP
FTP
SMTP
HTTP
FTP
Data
Data
H5
Application Layer
to Transport
from Transport
Data
H5
Data
Logical communication

## Slide 98: Transport Layer
Duties/services
  Port addressing
  Segmentation and reassembly
  Connection control
  Flow control (end-to-end)
  Error control (end-to-end)
Responsible for delivery of a message from one process to another

## Slide 99: Transport Layer
Transport Layer
Data
Data1
Data2
Data3
H4
H4
H4
to Network
Data
Data1
Data2
Data3
H4
H4
H4
from Network
(segments)
Process
Process
…
Process
Process
…
PORT #
PORT #

## Slide 100: Network Layer
Duties/services
  Logical addressing
  Routing
Responsible for the delivery of packets from the original source to the destination

## Slide 101: Network Layer
Network Layer
Data
from Transport
to Data Link
Data
to Transport
from Data Link
Data
H3
Data
H3
(packet)

## Slide 102: Network Layer
Network 1
Network 6
Network 5
1.1
1.2
6.6
6.1
6.3
5.7
5.2
Network 3
3.8
3.3
Router
Data
1.1
5.7
1.1, 1.2, 6.1, 5.7, ... are logical addresses
R1
R3
R2

## Slide 103: Data Link Layer
Duties/services
  Framing
  Physical addressing
  Flow control (hop-to-hop)
  Error control (hop-to-hop)
  Access control
Responsible for transmitting frames from one node to the next

## Slide 104: Data Link Layer
Data Link Layer
Data
from Network
to Physical
Data
to Network
from Physical
Data
H2
Data
H2
(frame)
T2
T2

## Slide 105: Data Link Layer
3B
A3, 3B, 82, 9F, ... are physical addresses
9F
82
A3
Data
9F
T2
A3
Data
H2

## Slide 106: Data Link Layer
Network 1
Network 6
Network 5
1.1
1.2
6.6
6.1
6.3
5.7
5.2
Network 3
3.8
3.3
Data
1.1
5.7
97
32
25
79
62
54
74
12
88
Data
1.1
5.7
25
97
Data
1.1
5.7
62
79
Data
1.1
5.7
74
54
R1
R3
R2

## Slide 107: Physical Layer
Duties/services
  Physical characteristics of interfaces and media
  Representation of bits
  Data rate (transmission rate)
  Synchronization of bits
Responsible for transmitting individual bits from one node to the next

## Slide 108: Physical Layer
Physical Layer
Data
from Data Link
to Data Link
Data
01001011
01001011
Transmission medium
(bits)

## Slide 109: The Big Picture
L5 data
H5
L4 data
H4
L3 data
H3
L2 data
T2
H2
0111011010101001010101001
L5 data
H5
L4 data
H4
L3 data
H3
L2 data
T2
H2
0111010101010010101010101
5
4
3
2
1
5
4
3
2
1
Transmission medium

## Slide 110: Internet Model
Network
D.L.
P.L.
D.L.
P.L.
Network
D.L.
P.L.
D.L.
P.L.
Application
Transport
Network
Data Link
Physical
Application
Transport
Network
Data Link
Physical
Transmission medium
sender
router
router
receiver

## Slide 111: Internet Model

## Slide 112: Protocol Suites
112
A set of protocols must be constructed
  to ensure that the resulting communication system is complete and efficient
Each protocol should handle a part of communication not handled by other protocols
How can we guarantee that protocols work well together?
  Instead of creating each protocol in isolation, protocols are designed in complete, cooperative sets called suites or families
Notes: 112

## Slide 113: Internet Protocol Suite
Layer | Protocols
Application | HTTP, FTP, Telnet, SMTP, ...
Transport | TCP, UDP, SCTP, ...
Network | IP (IPv4), IPv6, ICMP, IGMP, ...
Data Link | Ethernet, Wi-Fi, PPP, ...
Physical | RS-232, DSL, 10Base-T, ...

## Slide 114: OSI Model
OSI – Open Systems Interconnection
Developed by the International Standards Organizations (ISO)
Two additional layers
  Presentation layer
  Session layer
7.Application Layer
6.Presentation Layer
5.Session Layer
4.Transport Layer
3.Network Layer
2.Data Link Layer
1.Physical Layer
User
Transmission Medium

## Slide 115: Session Layer
Duties/services
  Interaction management
     Simplex, half-duplex, full-duplex
  Session recovery
Responsible for establishing, managing and terminating connections between applications

## Slide 116: Presentation Layer
Duties/services
  Data translation
  Encryption
  Decryption
  Compression
Responsible for handling differences in data representation to applications

## Slide 117: OSI Layers in Real World
transmission medium
Reads the message
Summarizes or translates letter
Opens letter
Withdraws letter from mailbox
Checks address and sorts letter
Unpacks packages
Unloads from truck
Handwrites a message
7.Manager
Prepares final version
6.Assistant
Provides address and packs letter
5.Secretary
Delivers letter to post office
4.Driver
Checks address and sorts letter
3.Postal staff
Packs letters for certain directions
2.Postal staff
Loads on truck
1.Postal staff
Pictures from Wikipedia