## Slide 1: IPv4 and IPv6 - Binary Conversion
IPv4 address | 192.168.50.112 /24 |  |  | 
Address in binary | 11000000.1010100.00110010.01110000 |  |  | 
Netmask in binary | 11111111.11111111.11111111.00000000 |  |  | 
IPv6 address | 2001:2EB8:ADC1:54ED:1100:697A:3210:3331 /64 |  |  |  |  |  |  | 
converted to binary | 0010-0000-0000-0001:0010-1110-1011-1000:1010-1101-1100-0001:0101-0100-1110-1101:0001-0001-0000-0000:0110-1001-0111-1010:0011-0010-0001-0000:0011-0011-0011-0001 |  |  |  |  |  |  | 

## Slide 2: IPv6
Global unicast address | 2001:2EB8:ADC1:54ED:1100:697A:3210:3331 /64 |  |  |  |  |  |  | 
Link-local address | FE80::1100:697A:3210:3331 /10 |  |  |  |  |  |  | 
128 bit address colon separated hexadecimal notation (8 hextets)
Link-local address on each interface (locally significant only)
Multiple routable addresses allowed on each interface
  Global unicast - unicast, routable on the Internet
  Unique local - unicast, similar to IPv4 private address
  Anycast - the same unicast address on multiple devices
Multicast addresses (no broadcast addresses)
/Network prefix - in slash decimal notation /64 (no subnet masks)

## Slide 3: IPv6 Network Prefix
 | Network (64 bits) |  |  |  | Interface ID |  |  | 
Global unicast address | 2001:2EB8:ADC1:54ED:1100:697A:3210:3331 /64 |  |  |  |  |  |  | 
 | Network (96 bits) |  |  |  |  | Interface ID |  | 
Global unicast address | 2001:2EB8:ADC1:54ED:0000:0000:0000:0F31 /96 |  |  |  |  |  |  | 
 | Network (128 bits - single host/network of one) |  |  |  |  |  |  | 
Global unicast address | 2001:2EB8:ADC1:54ED:0000:0000:0000:0F31 /128 |  |  |  |  |  |  | 
The network prefix separates the network portion from the interface ID
The network prefix refers to the number of bits in the network portion

## Slide 4: IPv6 Global Unicast Address
The network portion of the global unicast address is hierarchically structured
2001 | 00A1 | 2233 | 0001 | 0800:27FF:FE00:0008 | /64
Global Routing Prefix |  |  | Subnet | Interface ID | prefix
/64 subnet prefix
/48 site prefix
/32 provider prefix
/23 regional registry
/3 IANA global prefix

## Slide 5: IPv6 Address Compression
global address | 2001:0EB8:00C1:2200:0001:0000:0000:0331 /64 |  |  |  |  |  |  | 
leading zeros | 2001:0EB8:00C1:2200:0001:0000:0000:0331 /64 |  |  |  |  |  |  | 
continuous zeros | 2001:0EB8:00C1:2200:0001:0000:0000:0331 /64 |  |  |  |  |  |  | 
compressed | 2001:EB8:C1:2200:1::331 /64 |  |  |  |  |  |  | 
Leading zeros can be omitted (trailing zeros cannot)
A single instance of continuous zeros can be replaced with a double colon ::
When decompressing remember there are supposed to be 8 hextets of 4 hexadecimal characters each

## Slide 6: IPv6 SLAAC - Stateless Address Autoconfiguration
Router Solicitation (RS)
Router Advertisement (RA)
Neighbor Solicitation (NS) DAD
Autoconfigure address (EUI-64 or random)
1
2
3
4

## Slide 7: IPv6 SLAAC
RFC 4861 Neighbor Discovery - SLAAC - ICMPv6 |  |  | 
Message | Source address | Destination address | Type
Router Solicitation (RS) | unspecified address :: /128 | all-routers multicast FF02::2 | 133
Router Advertisement (RA) sent periodically, sent in response to a router solicitation (RS) | router link-local FE80::x | all-nodes multicast FF02::1 | 134
 | IPv6 prefixes (one or more) | 2000:1234:ABCD:EF22:: /64 | 
 | Router lifetime information | 0 (not default), 1 - 9000 seconds | 
 | flag information | M = managed, O = other (DHCPv6) | 
 | gateway / source address | FE80::x | 
1
2

## Slide 8: IPv6 SLAAC (EUI-64)
Autoconfigure address (EUI-64)
3
48 bit MAC Address |  |  | 08-00-27-00-00-08
split address in the middle |  |  | 08-00-27 00-00-08
insert FF:FE |  |  | 08-00-27 FF:FE 00-00-08
hexadecimal |  |  | 08-00-27 FF:FE 00-00-08
7th bit in binary |  |  | 00001000
7th bit flip changes 8 to A |  |  | 00001010
64 bit host interface ID |  |  | 0A00:27FF:FE00:0008

## Slide 9: IPv6 SLAAC
RFC 4861 Neighbor Discovery - SLAAC - ICMPv6 |  |  | 
Message | Source address | Destination address | Type
Neighbor Solicitation (NS) Similar to ARP in IPv6 check host availability check for DAD | link-local or unspecified address :: /128 if duplicate address detection (DAD) | all-solicited nodes multicast FF02::1:FFxx:xxxx | 135
Neighbor Advertisement (NA) response to (NS), used to announce a link-layer address change | link-local address FE80::x | link-layer address, or all-nodes multicast FF02::1 | 136
 |  | R=router flag-neighbor unreach S=solicited flag-response to NS O=override flag-update address | 
4

## Slide 10: IPv6 Address Types
Type | Purpose | Prefix
Global Unicast | routable on the Internet | 2000:: /3
Link Local | local link/network (only) | FE80:: /10
Multicast | sending to groups (no broadcast) | FF00:: /8
Unique Local | routable on a LAN (private address) | FC00::/8 FD00::/8
Modified EUI-64 | converts 48 bit MAC to 64 bit host ID | 7th bit flipped + FF:FE inserted
Autoconfiguration | stateless address autoconfiguration (SLAAC) | RS RA NS NA (ICMPv6)
Anycast | shared address, used to send to nearest available device interface | syntactically identical to unicast (identified as anycast) 2001:DB8:1::/64 (all zeros ID)

## Slide 11: IPv6 Addresses
IPv6 Address | Purpose
::/0 | all networks - used for default route
::1/128 | loopback - similar to 127.0.0.1
::/128 | unspecified address - no address yet
FE80::/10 | link-local
FF02::1 | all-nodes multicast
FF02::2 | all-routers multicast
FF02::1:FFxx:xxxx | All-solicited nodes multicast - autoconfiguration and neighbor discovery (similar to ARP)

## Slide 12: Router IPv6 Address Configuration
Router# configure terminal
Router(config)# ipv6 unicast-routing
Router(config)# interface g0/0
Router(config-if)# ipv6 address 2001:db8:22:1::1/64
or ipv6 address 2001:db8:22:1::/64 eui-64
Router(config-if)# ipv6 address fe80::1 link-local
Router(config-if)# no shutdown
Router(config-if)# interface g0/1
Router(config-if)# ipv6 enable
Router(config-if)# ipv6 address autoconfig
Router(config-if)# no shutdown
Router(config-if)# exit
Router(config)# interface g0/0
Router(config-if)# no ipv6 address 2001:db8:22:1::1/64
Router(config-if)# no ipv6 address fe80::1 link-local
Router(config-if)# shutdown