## Slide 1: IPv6 Routing Protocols

## Slide 2: Routing Protocols for IPv6
The IPv6 routing table is generated like in IPv4
It contains various information:
Prefix
Prefix length
Next hop
Route source (protocols)
Next-hop interface
metric

## Slide 3: Routing Protocols for IPv6
RIPng
RIPng (next generation) was created for IPv6
Distance Vector Routing Protocol
Open standard, supported by all vendors
Metric (cost) is hop count – maximum is 16
Concept equal to RIPv1 and RIPv2 for IPv4

## Slide 4: Routing Protocols for IPv6
RIPng
Limitations (same as with IPv4):
Network diameter can me a maximum of 15 hops
Metric does not care about link speed
Slow convergence
Thus, RIP and RIPng are not recommended routing protocols

## Slide 5: Routing Protocols for IPv6
OSPFv3
Link-State Routing Protocol
Supports IPv6 and IPv4
Open standard, supported by all vendors
Scalable, stable and proven

## Slide 6: Routing Protocols for IPv6
OSPFv3 – Differences to OSPFv2 (IPv4) – Part 1
Router LSA, Network LSA and Router ID stay 32 bit, so no IPv6 address can be used for these
Processing happens per link (interface) and not per subnet, because a single link possibly contains multiple IPv6 networks
Multiple OSPF instances per link are possible

## Slide 7: Routing Protocols for IPv6
OSPFv3 – Differences to OSPFv2 (IPv4) – Part 2
Communication happens over Link-Local addresses (per link) except for Virtual Link (global address are used as source)
Authentication via IPv6-Integrated IPsec AH, not in OSFP itself
OSPF packets are encapsulated directly into IPv6, no more TCP or UDP
Next Header field contains protocol number 89

## Slide 8: Routing Protocols for IPv6
OSPFv3 – New LSA Types
OSPFv3 | OSPFv2
0x2001 Router LSA | 1 Router LSA
0x2002 Network LSA | 2 Network LSA
0x2003 Inter-Area-Prefix LSA | 3 Network Summary LSA
0x2004 Inter-Area-Router LSA | 4 ASBR Summary LSA
0x2005 AS-External LSA | 5 AS-External LSA
0x2006 MOSPF LSA (deprec.) | 6 Group Membership LSA
0x2007 NSSA LSA | 7 NSSA External LSA
0x2008 Link LSA | 
0x2009 Inter-Area-Prefix LSA | 

## Slide 9: Routing Protocols for IPv6
EIGRP for IPv6
Link-State Routing Protocol
Cisco proprietary standard
Scalable, Stable, and proven

## Slide 10: Routing Protocols for IPv6
EIGRP for IPv6 – Differences to EIGRP for IPv4 – Part 1
Router ID stays 32 bit, no IPv6 address configurable
Process does not start , until a Router ID has been set
No Auto Summary, because IPv6 is always classless
No Split Horizon, because interfaces can have multiple prefixes
Explicit “no shutdown” in the EIGRP process is needed on start

## Slide 11: Routing Protocols for IPv6
EIGRP for IPv6 – Differences to EIGRP for IPv4 – Part 2
Source address of the Hello Packet is the Link-Local address, target is multicast group ff02::a (all EIGRP routers)
Updates are sent via unicast to the specific neighbor
Authentication can be MD5 (or IPsec – not available yet)

## Slide 12: Routing Protocols for IPv6
BGP
Current Version is BGP4
Path Vector Routing Protocol
Routing Protocol used on the internet
Also very common in MPLS VPNs
Multi Protocol Extension for IPv6 is available

## Slide 13: Routing Protocols for IPv6
BGP
Configuration via “address-families” (e.g. IPv4 unicast and IPv6 unicast, or VPN4/VPN6 for MPLS)
Separate peerings for IPv4 and IPv6 possible (recommended)
Single peering to transports multiple address families over either IPv6 and IPv4 also possible
Functions identical to IPv4

## Slide 14: Routing Protocols for IPv6
BGP
Why are separate peerings preferred?
Next-hop for routes does not have to be set manually
No risk of losing both IPv4 and IPv6, if transport protocol fails

## Slide 15: Routing Protocols for IPv6
IS-IS
Link State Routing Protocol
Similar to OSPF (also uses Dijkstra Algorithm)
Works on top of Layer 2 instead of Layer 3, thus protocol independent and IPv6-capable without modification
Commonly used by ISPs
Is also used for 802.1aq Shortest Path Bridging (SPB, replacement for Spanning Tree)