## Slide 1: Signal Dispersion in Fibers

## Slide 2
An optical signal weakens from attenuation mechanisms and broadens due to dispersion effects as it travels along a fiber.
Eventually these two factors will cause neighboring pulses to overlap.
After a certain amount of overlap occurs, the receiver can no longer distinguish the individual adjacent pulses and errors arise when interpreting the received signal

## Slide 4: Overview of Dispersion Origins
Signal dispersion is a consequence of factors such as intermodal delay (also called intermodal dispersion), intramodal dispersion, polarization-mode dispersion, and higher-order dispersion effects.
These distortions can be explained by examining the behavior of the group velocities of the guided modes, where the group velocity is the speed at which energy in a particular mode travels along the fiber

## Slide 5: Intermodal delay
Intermodal delay (or simply modal delay) appears only in multimode fibers.
Modal delay is a result of each mode having a different value of the group velocity at a single frequency.

## Slide 6: Intramodal dispersion
Intramodal dispersion or chromatic dispersion is pulse spreading that takes place within a single mode.
This spreading arises from the finite spectral emission width of an optical source.
The phenomenon also is known as group velocity dispersion, since the dispersion is a result of the group velocity being a function of the wavelength.
Because intramodal dispersion depends on the wavelength, its effect on signal distortion increases with the spectral width of the light source.
The spectral width is the band of wavelengths over which the source emits light.
This wavelength band normally is characterized by the root-meansquare (rms) spectral width.
Depending on the device structure of a light-emitting diode (LED), the spectral width is approximately 4 to 9 percent of a central wavelength.
For example, as Fig. illustrates, if the peak wavelength of an LED is 850 nm, a typical source spectral width would be 36 nm; that is, such an LED emits most of its light in the 832-to-868-nm wavelength band.
Laser diode optical sources exhibit much narrower spectral widths, with typical values being 1–2 nm for multimode lasers and 10-4 nm for single-mode lasers

## Slide 8
The two main causes of intramodal dispersion are as follows:
Material dispersion arises due to the variations of the refractive index of the core material as a function of wavelength.
Material dispersion also is referred to as chromatic dispersion, since this is the same effect by which a prism spreads out a spectrum.
This refractive index property causes a wavelength dependence of the group velocity of a given mode; that is, pulse spreading occurs even when different wavelengths follow the same path.

## Slide 10
Waveguide dispersion causes pulse spreading because only part of the optical power propagation along a fiber is confined to the core.
Within a single propagating mode, the cross-sectional distribution of light in the optical fiber varies for different wavelengths.
Shorter wavelengths are more completely confined to the fiber core, whereas a larger portion of the optical power at longer wavelengths propagates in the cladding.
The refractive index is lower in the cladding than in the core, so the fraction of light power propagating in the cladding travels faster than the light confined to the core.
The index of refraction depends on the wavelength so that different spectral components within a single mode have different propagation speeds.

## Slide 11
Dispersion thus arises because the difference in core-cladding spatial power distributions, together with the speed variations of the various wavelengths, causes a change in propagation velocity for each spectral component.
The degree of waveguide dispersion depends on the fiber design.
Waveguide dispersion usually can be ignored in multimode fibers, but its effect is significant in single-mode fibers.

## Slide 13: Polarization-mode dispersion
Polarization-mode dispersion results from the fact that light-signal energy at a given wavelength in a single-mode fiber actually occupies two orthogonal polarization states or modes.
At the start of the fiber the two polarization states are aligned.
However, since fiber material is not perfectly uniform throughout its length, each polarization mode will encounter a slightly different refractive index.
Consequently each mode will travel at a slightly different velocity.
The resulting difference in propagation times between the two orthogonal polarization modes will cause pulse spreading.

## Slide 42: Modal Delay
Intermodal dispersion or modal delay appears only in multimode fibers.
This signal-distorting mechanism is a result of each mode having a different value of the group velocity at a single frequency.
The steeper the angle of propagation of the ray congruence, the higher is the mode number and, consequently, the slower the axial group velocity.
This variation in the group velocities of the different modes results in a group delay spread, which is the intermodal dispersion.

## Slide 43
Intermodal Dispersion
Exists in multimode fiber cable
It causes the input light pulse to spread.
Light Pulse consists of group of modes. The light energy is delayed with different amount
along the fiber.

## Slide 44
This dispersion mechanism is eliminated by single-mode operation but is important in multimode fibers.
The maximum pulse broadening arising from the modal delay is the difference between the travel time Tmax of the longest ray congruence paths (the highest-order mode) and the travel time Tmin of the shortest ray congruence paths (the fundamental mode).
This broadening is simply obtained from ray tracing and for a fiber of length L is given by

## Slide 45
The fiber capacity is specified in terms of the bit rate-distance product BL, that is, the bit rate times the possible transmission distance L. In order for neighboring signal pulses to remain distinguishable at the receiver, the pulse spread should be less than 1/B, which is the width of a bit period.

## Slide 47
The root-mean-square (rms) value of the time delay is a useful parameter for assessing the effect of modal delay in a multimode fi ber.
If it is assumed that the light rays are uniformly distributed over the acceptance angles of the fiber, then the rms impulse response ss due to intermodal dispersion in a step index multimode fiber can be estimated from the expression.

## Slide 48
A successful technique for reducing modal delay in multimode fibers is through the use of a graded refractive index in the fiber core.
In any multimode fiber the ray paths associated with higher-order modes are concentrated near the edge of the core and thus follow a longer path through the fiber than lower-order modes (which are concentrated near the fiber axis).
However, if the core has a graded index, then the higher-order modes encounter a lower refractive index near the core edge.
Since the speed of light in a material depends on the refractive index value, the higher-order modes travel faster in the outer core region than those modes that propagate through a higher refractive index along the fi ber center.
Consequently this reduces the delay difference between the fastest and slowest modes.

## Slide 49
absolute modal delay at the output of a graded-index fiber that has a parabolic core index profile

## Slide 57: Birefringence in single-mode fibers
Because of asymmetries the refractive indices for the two degenerate modes (vertical & horizontal polarizations) are different. This difference is referred to as birefringence, :
Optical Fiber communications, 3rd ed.,G.Keiser,McGrawHill, 2000

## Slide 58: Fiber Beat Length
In general, a linearly polarized mode is a combination of both of the degenerate modes. As the modal wave travels along the fiber, the difference in the refractive indices would change the phase difference between these two components & thereby the state of the polarization of the mode. However after certain length referred to as fiber beat length, the modal wave will produce its original state of polarization. This length is simply given by:
[2-35]

## Slide 59
Modal Birefringence

## Slide 60
Intermodal Dispersion
Exists in multimode fiber cable
It causes the input light pulse to spread.
Light Pulse consists of group of modes. The light energy is delayed with different amount
along the fiber.

## Slide 62: Graded Index Fiber Structure
In graded index fiber, core refractive index decreases continuously with increasing radial distance r from center of fiber and constant in cladding
α defines the shape of the index profile
As α goes to infinity, above reduces to step index
The index difference is

## Slide 63: contd
NA is more complex than step index fiber since it is function of position across the core
Geometrical optics considerations show that light incident on fiber core at position r will propagate only if it within NA(r)
Local numerical aperture is defined as
And

## Slide 64: Examples
If a = 9.5 micron, find n2 in order to design a single mode fiber, if n1=1.465.
Solution,
The longer the wavelength, the larger refractive index difference is needed to maintain single mode condition, for a given fiber

## Slide 65: Examples
Compute the number of modes for a fiber whose core diameter is 50 micron. Assume that n1=1.48 and n2=1.46. Wavelength = 0.8 micron.
Solution
For large V, the total number of modes supported can be estimated as

## Slide 66: Example
What is the maximum core radius allowed for a glass fiber having n1=1.465 and n2=1.46 if the fiber is to support only one mode at wavelength of 1250nm.
Solution