## Slide 1: UNIT IV DATA LINK LAYER
Medium Access Control Techniques
A mechanism which provides a link with reliable communication.
There is an available dedicated link(or channel) between the sender and the receiver.
Example: if we use our cellular phone to connect to another cellular phone, the channel( the band allocated to the vendor company) is not dedicated.
It has two sublayers.
Upper sublayer is responsible for data link control.
Lower sublayer is responsible for resolving access to the shared media.

## Slide 2: Data link layer divided into two functionality-oriented sublayers
The upper sublayer is responsible for flow and error control is called Logical Link Control(LLC) layer.
The lower sublayer is responsible for multiple access resolution is called the media access control (MAC) layer.
When nodes or stations are connected and use a common link called a multipoint or broadcast link, we need a multiple access protocol to coordinate access to the link.
Eg: assembly.

## Slide 3: Taxonomy of multiple-access protocols

## Slide 4: CONTROLLED ACCESS
In controlled access, the stations consult one another to find which station has the right to send.
A station cannot send unless it has been authorized by other stations.
Three popular controlled-access methods.
Reservation
Polling
Token Passing

## Slide 5: Reservation
In the reservation method, a station needs to make a reservation before sending data.
Time is divided into intervals. In each interval, a reservation frame precedes the data frames in that interval.
If there are N stations in the system, there are exactly N reservation minislots in the reservation frame. Each minislot belongs to a station.

## Slide 6: Polling
It works with topologies in which one device is designated as a primary station and the other devices are secondary stations.
The primary device controls the link.
The secondary devices follow its instructions.
Primary device is to determine which device is allowed to use the channel at a given time.(initiator of a session).
If the primary wants to receive data, it asks the secondaries if they have anything to send, this is called poll function.(poll)
If the primary wants to send data, it tells the secondary to get ready to receive, this is called select function.(SEL)

## Slide 7: Select and poll functions in polling access method

## Slide 8: Token Passing
The stations in a network are organized in a logical ring.
For each station, there is a predecessor and a successor.
A special packet called a token circulates through the ring.
Token management, the token must be monitored to ensure it has not been lost or destroyed.
Logical ring and physical topology in token-passing access method

## Slide 9: RANDOM ACCESS
In random access or contention methods, no station is superior to another station and none is assigned the control over another.
No station permits, or does not permit, another station to send.
At each instance, a station that has data to send uses a procedure defined by the protocol to make a decision on whether or not to send.
Two features
There is no schedule time for a station to transmit. Transmission is random among the stations.
No rules specify which station should send next. Stations compete with one another to access the medium
If more than one station tries to send, there is an access conflict-Collision and the frames will be either destroyed or modified.

## Slide 10
ALOHA, protocol which is used a very simple procedure called multiple access.
The method was improved with the procedure that forces the station to sense the medium before transmitting. This was called Carrier Sense Multiple Access
Carrier Sense Multiple Access with Collision Detection(CSMA/CD)
Carrier Sense Multiple Access with Collision Avoidance (CSMA/CA)
ALOHA
It was designed for a radio(wireless) LAN, but it can be used on any shared medium.
Types of ALOHA
Pure ALOHA
Slotted ALOHA
Pure ALOHA(original ALOHA)
Each station sends a frame whenever it has a frame to send.
We need to mention that even if one bit of a frame coexists on the channel with one bit from another frame, there is a collision and both will be destroyed.

## Slide 11
Frames in a pure ALOHA network
Need to resend the frames that have been destroyed during transmission.
Acknowledgement(time-out period)
Methods to prevent collision:
Back-off time TB.(random amount of time)
After a maximum number of retransmission attempts Kmax, a station must give up and try later.

## Slide 12
Procedure for pure ALOHA protocol
Time out = maximum possible round-trip propagation delay, which is twice the amount of time required to send a frame between separated stations(2*TP)

## Slide 13: Example: The stations on a wireless ALOHA network are a maximum of 600 km apart. If we assume that signals propagate at 3 × 108 m/s, we find Tp = (600 × 105 ) / (3 × 108 ) = 2 ms. Now we can find the value of TB for different values of K .
a. For K = 1, the range is {0, 1}. The station needs to generate a random number with a value of 0 or 1. This means that TB is either 0 ms (0 × 2) or 2 ms (1 × 2),based on the outcome of the random variable.
b. For K = 2, the range is {0, 1, 2, 3}. This means that TB can be 0, 2, 4, or 6 ms, based on the outcome of the random variable.
c. For K = 3, the range is {0, 1, 2, 3, 4, 5, 6, 7}. This means that TB can be 0, 2, 4, . . . , 14 ms, based on the outcome of the random variable.
d. We need to mention that if K > 10, it is normally set to 10.

## Slide 14
Vulnerable time for pure ALOHA protocol

## Slide 15
A pure ALOHA network transmits 200-bit frames on a shared channel of 200 kbps. What is the requirement to make this frame collision-free?
Example for vulnerable time
Solution
Average frame transmission time Tfr is 200 bits/200 kbps or 1 ms. The vulnerable time is 2 × 1 ms = 2 ms. This means no station should send later than 1 ms before this station starts transmission and no station should start sending during the one 1-ms period that this station is sending.
Throughput
Let G be the average number of frames generated by the system during one frame transmission time.
The average number of successful transmission for pure ALOHA is S = G × e −2G
The maximum throughput Smax = 0.184 when G= (1/2).
If one half a frame is generated during one frame transmission time, then 18.4% of these frames reach their destination successfully.

## Slide 16
A pure ALOHA network transmits 200-bit frames on a shared channel of 200 kbps. What is the throughput if the system (all stations together) produces
a. 1000 frames per second b. 500 frames per second c. 250 frames per second.
Example for throughput
Solution
The frame transmission time is 200/200 kbps or 1 ms.
If the system creates 1000 frames per second, the load is 1. in this case S=G × e−2 G or S=0.135(13.5%). This means that the throughput is 1000 X 0.135=135 frames. Only 135 frames out of 1000 will probably survive.
If the system creates 500 frames per second, the load is 1/2. in this case S=G × e−2 G or S=0.184(18.4%). This means that the throughput is 500 X 0.184=92 frames. Only 92 frames out of 500 will probably survive.
If the system creates 250 frames per second, the load is 1/4. in this case S=G × e−2 G or S=0.152(15.2%). This means that the throughput is 250 X 0.152=38 frames. Only 38 frames out of 250 will probably survive.

## Slide 17: Slotted ALOHA
In slotted ALOHA, we divide the time into slots of Tfr and force the station to send only at the beginning of the time slot.
If a station misses the moment, it must wait until the beginning of the next time slot.
The station which started at the beginning of this slot has already finished sending its frame.
Collision
If two stations try to send at the beginning of the same time slot.
However the vulnerable time is now reduced to one-half, equal to Tfr.
Slotted ALOHA vulnerable time = Tfr

## Slide 18
Frames in a slotted ALOHA network

## Slide 19: Throughput
The throughput for slotted ALOHA is S = G × e−G .
The maximum throughput Smax = 0.368 when G = 1.
Vulnerable time for slotted ALOHA protocol

## Slide 20
A slotted ALOHA network transmits 200-bit frames on a shared channel of 200 kbps. What is the throughput if the system (all stations together) produces
a. 1000 frames per second b. 500 frames per second c. 250 frames per second.
Example
Solution
The frame transmission time is 200/200 kbps or 1 ms.
If the system creates 1000 frames per second, the load is 1. in this case S=G × e−G or S=0.368(36.8%). This means that the throughput is 1000 X 0.368=368 frames. Only 368 frames out of 1000 will probably survive.
If the system creates 500 frames per second, the load is 1/2. in this case S=G × e−G or S=0.303(30.3%). This means that the throughput is 500 X 0.303=151 frames. Only 151 frames out of 500 will probably survive.
If the system creates 250 frames per second, the load is 1/4. in this case S=G × e−G or S=0.195(19.5%). This means that the throughput is 250 X 0.195=49 frames. Only 49 frames out of 250 will probably survive.

## Slide 21: Carrier Sense Multiple Access(CSMA)
CSMA requires that each station first listen to the medium before sending.( Sense before transmit)
It can reduce the possibility of collision, but it cannot eliminate it.
The possibility of collision still exists because of propagation delay.
A station may sense the medium and find it idle, only because the first bit sent by another station has not yet been received.
At time t1, station B senses the medium and find it idle, so it sends a frame.
At time t2(t2>t1), station c senses the medium and finds it idle because at this time, the first bits from station B have not reached station C. station C also sends a frame.
The two signals collide and both frames are destroyed.

## Slide 22
Figure Space/time model of the collision in CSMA

## Slide 23
Vulnerable time in CSMA
Propagation time Tp- time needed for a signal to propagate from one end of the medium to the other.
The leftmost station A sends a frame at time t1, which reaches the rightmost station D at time t1+Tp.

## Slide 24: Persistence Methods
What should a station do if the channel is busy or is idle?
1-Persistent(Probability 1)
After the station finds the line idle, it sends its frame immediately. This method has the highest chance of collision.
NonPersistent
A station that has a frame to send senses the line. If the line is idle, it sends immediately. If the line is not idle, it waits a random amount of time and then senses the line again.
It reduces the chance of collision and it reduces the efficiency of the network.
p-Persistent
This method is used if the channel has time slots with a slot duration equal to or greater than the maximum propagation time.
It combines the advantages of the other two methods.
It reduces the chance of collision and improves efficiency

## Slide 25
With probability p, the station sends its frame.
With probability q=1-p, the station waits for beginning of the next time slot and checks the line again

## Slide 26
Figure Flow diagram for three persistence methods

## Slide 27
CSMA/CD

## Slide 28
Figure Collision and abortion in CSMA/CD

## Slide 29
A network using CSMA/CD has a bandwidth of 10 Mbps. If the maximum propagation time (including the delays in the devices and ignoring the time needed to send a jamming signal, as we see later) is 25.6 μs, what is the minimum size of the frame?
Example
Solution
The frame transmission time is Tfr = 2 × Tp = 51.2 μs. This means, in the worst case, a station needs to transmit for a period of 51.2 μs to detect the collision. The minimum size of the frame is 10 Mbps × 51.2 μs = 512 bits or 64 bytes. This is actually the minimum size of the frame for Standard Ethernet.
Throughput
The maximum throughput occurs at a different value of G and is based on the persistence method.
For 1-persistent method the maximum throughput is around 50% when G=1.
For nopersistent method, the maximum throughput can go up to 90% when G is between 3 and 8.

## Slide 30
Flow diagram for the CSMA/CD

## Slide 31
Energy level during transmission, idleness, or collision

## Slide 32: CSMA/CA
Interframe space(IFS)
When an idle channel is found, the station does not send immediately. It waits for a period of time(IFS).
In CSMA/CA, the IFS can also be used to define the priority of a station or a frame.
Contention window
The contention window is an amount of time divided into slots. A station that is ready to send chooses a random number of slots as its wait time.
The number of slots in the window changes according to the binary exponential back off strategy.
In CSMA/CA, if the station finds the channel busy, it does not restart the timer of the contention window; it stops the timer and restarts it when the channel becomes idle.

## Slide 33
Figure Timing in CSMA/CA
Acknowledgement
With all these precautions, there still may be a collision resulting in destroyed data.
The data may be corrupted during the transmission.
The positive acknowledgement and the time-out timer can help guarantee that the receiver has received the frame.

## Slide 34
Flow diagram for CSMA/CA

## Slide 35: FLOW AND ERROR CONTROL
Flow control refers to a set of procedures used to restrict the amount of data that the sender can send before waiting for acknowledgment.
Error control in the data link layer is based on automatic repeat request, which is the retransmission of data.
ARQ types
Stop-and-Wait Automatic Repeat Request
Go-Back-N Automatic Repeat Request
Selective Repeat Automatic Repeat Request

## Slide 36: Stop-and-Wait Automatic Repeat Request
Error correction in Stop-and-Wait ARQ is done by keeping a copy of the sent frame and retransmitting of the frame when the timer expires.
In Stop-and-Wait ARQ, we use sequence numbers to number the frames. The sequence numbers are based on modulo-2 arithmetic.
In Stop-and-Wait ARQ, the acknowledgment number always announces in modulo-2 arithmetic the sequence number of the next frame expected.

## Slide 37
Design of the Stop-and-Wait ARQ Protocol

## Slide 38
Sender-site algorithm for Stop-and-Wait ARQ

## Slide 39
Sender-site algorithm for Stop-and-Wait ARQ

## Slide 40
Receiver-site algorithm for Stop-and-Wait ARQ Protocol

## Slide 41
shows an example of Stop-and-Wait ARQ. Frame 0 is sent and acknowledged. Frame 1 is lost and resent after the time-out. The resent frame 1 is acknowledged and the timer stops. Frame 0 is sent and acknowledged, but the acknowledgment is lost. The sender has no idea if the frame or the acknowledgment is lost, so after the time-out, it resends frame 0, which is acknowledged.
Example 1

## Slide 42
Flow diagram

## Slide 43: Go-Back-N Automatic Repeat Request
In the Go-Back-N Protocol, the sequence numbers are modulo 2m, where m is the size of the sequence number field in bits.
The send window is an abstract concept defining an imaginary box of size 2m − 1 with three variables: Sf, Sn, and Ssize.
The send window can slide one or more slots when a valid acknowledgment arrives.

## Slide 44
Send window for Go-Back-N ARQ

## Slide 45
Receive window for Go-Back-N ARQ

## Slide 46
Design of Go-Back-N ARQ

## Slide 47
Window size for Go-Back-N ARQ
In Go-Back-N ARQ, the size of the send window must be less than 2m;
the size of the receiver window is always 1.

## Slide 48
Algorithm Go-Back-N sender algorithm

## Slide 49
Algorithm Go-Back-N sender algorithm

## Slide 50
Algorithm Go-Back-N receiver algorithm

## Slide 51
Flow diagram

## Slide 52: Comparison of Go-Back-N and Selective Repeat
Go-Back-N Protocol and “Selective Repeat Protocol” are the sliding window protocols. The sliding window protocol is primarily an error control protocol
The basic difference between go-back-n protocol and selective repeat protocol is that the “go-back-n protocol” retransmits all the frames that lie after the frame which is damaged or lost. The “selective repeat protocol” retransmits only that frame which is damaged or lost.

## Slide 53: Go-Back-N

## Slide 54: Selective Repeat

## Slide 55
BASIS FOR COMPARISON | GO-BACK-N | SELECTIVE REPEAT
Basic | Retransmits all the frames that sent after the frame which suspects to be damaged or lost. | Retransmits only those frames that are suspected to lost or damaged.
Bandwidth Utilization | If error rate is high, it wastes a lot of bandwidth. | Comparatively less bandwidth is wasted in retransmitting.
Complexity | Less complicated. | More complex as it require to apply extra logic and sorting and storage, at sender and receiver.
Window size | N-1 | <= (N+1)/2
Sorting | Sorting is neither required at sender side nor at receiver side. | Receiver must be able to sort as it has to maintain the sequence of the frames.
Storing | Receiver do not store the frames received after the damaged frame until the damaged frame is retransmitted. | Receiver stores the frames received after the damaged frame in the buffer until the damaged frame is replaced.
ACK Numbers | NAK number refer to the next expected frame number. | NAK number refer to the frame lost.
Use | It more often used. | It is less in practice because of its complexity.

## Slide 56
Send window for Selective Repeat ARQ
Receive window for Selective Repeat ARQ

## Slide 57
Design of Selective Repeat ARQ

## Slide 58
Selective Repeat ARQ, window size
In Selective Repeat ARQ, the size of the sender and receiver window
must be at most one-half of 2m.

## Slide 59
Algorithm Sender-site Selective Repeat algorithm

## Slide 60
Algorithm Sender-site Selective Repeat algorithm

## Slide 61
Algorithm Sender-site Selective Repeat algorithm

## Slide 62
Algorithm Receiver-site Selective Repeat algorithm

## Slide 63
Algorithm Receiver-site Selective Repeat algorithm

## Slide 64
Figure Delivery of data in Selective Repeat ARQ

## Slide 65
BLOCK CODING
In block coding, we divide our message into blocks, each of k bits, called datawords. We add r redundant bits to each block to make the length n = k + r. The resulting n-bit blocks are called codewords.
To detect or correct errors, we need to send extra (redundant) bits with data.
Error Detection Error Correction Hamming Distance
Topics discussed in this section:

## Slide 66
Figure The structure of encoder and decoder

## Slide 67
Figure Process of error detection in block coding
Error Detection
The receiver has a list of valid codewords.
The original codeword has changed to an invalid one.
The codeword is corrupted during transmission but the received word still matches a valid codeword, the remains undetected.
This type of coding can detect only single errors

## Slide 68
Let us assume that k = 2 and n = 3. Table 10.1 shows the list of datawords and codewords (even parity). It is only good for detecting one bit error.
Example
A code for error detection
An error-detecting code can detect only the types of errors for which it is designed; other types of errors may remain undetected.

## Slide 69
Structure of encoder and decoder in error correction
Error Correction
It is much more difficult than error detection.
In error detection, the receiver needs to know only the received codeword is invalid; in error correction the receiver needs to find the original codeword sent.
It needs more redundant bits than error detection.

## Slide 70: Hamming Code
The Hamming distance between two words is the number of differences between corresponding bits.
It can easily be found if we apply the XOR operation on the two words and count the number of 1s in the result.
Let us find the Hamming distance between two pairs of words.
1. The Hamming distance d(000, 011) is 2 because
2. The Hamming distance d(10101, 11110) is 3 because

## Slide 71: Parity Check
A simple parity-check code is a single-bit error-detecting code in which n = k + 1 with dmin = 2.
K-bit dataword is changed to an n-bit codeword where n=k+1. the extra bit called the parity bit.

## Slide 72
Encoder and decoder for simple parity-check code
The result, which is called the syndrome, is just 1 bit.
The syndrome is 0 when the number of 1s in the received codeword is even; otherwise, it is 1.

## Slide 73
Two-dimensional parity-check code
Hamming Distance
The code were originally designed with dmin=3, which means that they can detect up to 2 errors or correct 1 single error.
We need to choose an integer m>=3. The values of n and k are then calculated from m as n=2m -1 and k=n-m. The number of check bits r = m.
If m=3, then n=7 and k=4. Hamming code C(7,4) with dmin =3.

## Slide 74
Two-dimensional parity-check code

## Slide 75
The structure of the encoder and decoder for a Hamming code

## Slide 76
Hamming code C(7, 4) - n=7, k = 4
Parity checks are created as follow (using modulo-2)
r0 = a2 + a1 + a0
r1 = a3 + a2 + a1
r2 = a1 + a0 + a3

## Slide 77
The checker in the decoder creates a 3-bit syndrome (s2 s1 s0).
In which each bit is the parity check for 4 out of the 7 bits in the received codeword:
s0 = b2 + b1 + b0 + q0
s1 = b3 + b2 + b1 + q1
s2 = b1 + b0 + b3 + q2
The equations used by the checker are the same as those used by the generator with the parity-check bits added to the right-hand side of the equation.

## Slide 78
Burst error correction using Hamming code
Split burst error between multiple codewords

## Slide 79
CHECKSUM
The last error detection method we discuss here is called the checksum. The checksum is used in the Internet by several protocols although not at the data link layer. However, we briefly discuss it here to complete our discussion on error checking
Idea One’s Complement Internet Checksum
Topics discussed in this section:

## Slide 80
Suppose our data is a list of five 4-bit numbers that we want to send to a destination. In addition to sending these numbers, we send the sum of the numbers. For example, if the set of numbers is (7, 11, 12, 0, 6), we send (7, 11, 12, 0, 6, 36), where 36 is the sum of the original numbers. The receiver adds the five numbers and compares the result with the sum. If the two are the same, the receiver assumes no error, accepts the five numbers, and discards the sum. Otherwise, there is an error somewhere and the data are not accepted.
Idea
Example
We can make the job of the receiver easier if we send the negative (complement) of the sum, called the checksum. In this case, we send (7, 11, 12, 0, 6, −36). The receiver can add all the numbers received (including the checksum). If the result is 0, it assumes no error; otherwise, there is an error.

## Slide 81: One’s Complement
We can represent unsigned numbers between 0 and 2n -1 using only n bits.
If the number has more than n bits, the extra leftmost bits need to be added to the n rightmost bits(Wrapping).
A negative number can be represented by inverting all bits.
Example
How can we represent the number 21 in one’s complement arithmetic using only four bits?
Solution
The number 21 in binary is 10101 (it needs five bits). We can wrap the leftmost bit and add it to the four rightmost bits. We have (0101 + 1) = 0110 or 6.

## Slide 82
How can we represent the number −6 in one’s complement arithmetic using only four bits?
Solution
In one’s complement arithmetic, the negative or complement of a number is found by inverting all bits. Positive 6 is 0110; negative 6 is 1001. If we consider only unsigned numbers, this is 9. In other words, the complement of 6 is 9.
Example

## Slide 83
1
1
1
0

## Slide 84: Internet Checksum
Sender site:
1. The message is divided into 16-bit words.
2. The value of the checksum word is set to 0.
3. All words including the checksum are added using one’s complement addition.
4. The sum is complemented and becomes the checksum.
5. The checksum is sent with the data.
Receiver site:
1. The message (including checksum) is divided into 16-bit words.
2. All words are added using one’s complement addition.
3. The sum is complemented and becomes the new checksum.
4. If the value of checksum is 0, the message is accepted; otherwise, it is rejected.

## Slide 85: Internet Checksum Example
When adding numbers, a carryout from the most significant bit needs to be added to the result
Example: add two 16-bit integers
1 1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
1 0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
wraparound
sum
checksum
Notes: Kurose and Ross forgot to say anything about wrapping the carry and adding it to low order bit